Crawford Panel Sectional door

Product description:

Overhead sectional door/sectional door with insulated panels filled with CFC-free polyurethan, panel thickness 42 mm, panel height 545 mm

Surface, waffled steel or aluminium sheet

Integrated finger pinch protection

Top, bottom and side seals and seals between door sections

Standard track system in galvanized steel

Spring balancing, 20.000 cycles

Spring break device

Lock bolt, step-handle,

Compliance with all operational and safety instructions in EU Directives and the standards of the European Standardization Committee (CEN)

Standard hardware (head room 485/510 mm to 800 mm)

Operating system: manual

Standard door sizes (DLW x DLH) MIN: 2.050 x 2.150 mm

MAX: 8.000 x 6.000 mm

Wind load (EN 12424)	Class 3 (700 N/m²) up to door 4.250 x 4.500 mm,

Class 2 (450 N/m²) up to door 8.000 x 6.000 mm.

Thermal transmittance (EN

12428)

W / (m² K) full panel door (steel)

W/(m²K) full panel door

1.25 W/(m² K) with window and passdoor

Water penetration (EN 12425) Class 3, (Door 4.000 x 4.000 mm)

Air permeability (EN 12426)	Class 2 (Door 4.000 x 4.000 mm + passdoor)

Dimensions:

x	mm (WxH) Glazing options:

Sandwich glazing, double glazed, rectangular, 600 x 290 mm

Sandwich glazing, double glazed, oval, 590 x 270 mm

Aluminium frame bar section with, acrylic sheets, 2 x 3 mm, total thickness 27 mm, single sealed

Aluminium frame bar section with, scratch resistant acrylic glass, 2 x 3 mm, total thickness 27 mm, single sealed

Aluminium frame bar section with, acrylic glass 2 x 3 mm, total thickness 27 mm, double sealed

Aluminium frame bar section with, scratch resistant acrylic glass 2 x 3 mm, total thickness 27 mm, double sealed

Aluminium frame bar section with, single glazing 3 mm acrylic

Aluminium frame bar section with, scratch resistant single glazing 3 mm acrylic

Aluminium frame bar section with, single glazing 4 mm hardened glass

Triple glazing – scratch resistant

Triple glazing – not scratch resistant

Surface colour:

Steel panel

	Standard: Polyester coating exterior RAL 1021, 3002, 5010, 6005, 7016, 9002, 9006,

9007, 9010, interior RAL 9002

Option: exterior painted in RAL and NCS-standard colour, buyer's choice

Option: exterior painted according to colour sample

Aluminium panel

Standard: Aluminium colour interior and exterior

Option: Polyester coating exterior RAL 5010, 9010, interior polyester transparent

Option: exterior painted in RAL and NCS -standard colour buyer's choice

Option: exterior painted according to colour sample

Passdoor:

Standard: opening outwards, door seals, Left or Right hinged, PC lock, doorway height 1850 mm, doorway width 900 mm, overhead door closer, profile of passdoor E6/EV1, glazing like rest of door, passdoor safety switch

Low threshold: opening outwards, door seals, DIN L or DIN R hinged, PC lock, doorway height 1850 mm, doorway width 900 mm, overhead door closer, profile of passdoor E6/ EV1, glazing like rest of door, passdoor safety switch

Option: PC lock with knob cylinder

Option: Nemef panic lock

Option: Nemef panic lock with panic bolt

Door locking device:

Option: Second lock bolt

Option: Lock with profile cylinder lockable on one or both sides

Option: Door locking switch (essential with electric operation)

Hardware:

Standard Low Lift (drop clearance 400 mm to 485/510 mm)

Low Lift (drop clearance 265/310 mm to 485/510 mm)

High Lift (drop clearance 800 mm to door height + 390 mm) - maximum lift 3.900 mm

Vertical Lift (drop clearance min. door height + 350 mm)

Operator:

Option: Chain hoist "T" (Gear ratio 1:4, Door weight max. 250 kg)

Option: Chain hoist "U" (Gear ratio 1:3, Door weight over 250 kg)

Option: Electronic operator:

Operating voltage: 230 V AC, 50/60 HZ (internal supply 3-phase 230 V AC)

Operating factor: ED = 30%, S3 10 min, non-continuous operation

(Engine operation 3 min, pause 7 min, direct-inverting)

Torque: 15-40 Nm, depending on reel type (value of given door shaft)

Fusing: 10 A

Brake: non-reversible worm gear

Speed monitor: electronic monitoring

Freewheel / clutch: mechanical engagement/disengagement

Limit switch: electronic via torque (setting "Door open" during programming) Setting "Door closed" in processor board

Gears: worm gear 1750 RPM yields approx. 24 rotations door shaft

Shaft: ø35 mm or hexagonal

Direct drive system

No special wall reinforcement necessary

Temperature range: -20°C to 60°C

Soft stop, soft start

Connection using "CEE plug"	or lockable mains isolator

Maximum door weight 400 kg

Options:

Chain transmission

Chain guard

Other drive variants available on request subject to technical inspection

Control units:

Control unit

Output 0.37 kW, input 1 x 230 V. Including control unit with standard actuator UP-STOP- DOWN. The door closes using dead-man controls.

Operating speed 0.25 m/s, safety rating IP 55. If there is a power failure, the disengage device enables manual operation at any time

Options:

Additional buttons, key switch

Door/bridge interlock

Control unit

Output 0.37 kW, input 1 x 230 V. Including control unit with standard actuator UP-STOP- DOWN. The door closes using pulse control incl. self-monitoring safety edge

Operating speed 0.25 m/s, safety rating IP 55. If there is a power failure, the disengage device enables manual operation at any time

Options:

Radio remote control

"Open" (if open button is used during closing process - door immediately stops and opens completely)

"Automatic close" (safety photo cell compulsory requirement)

Door closes automatically after set period (4-60 sec)

Pull switch for opening function

External push-button, key switch

Door/bridge interlock

Control unit

Output 0.37 kW, input 1 x 230 V. Dimensions: 180 x 380 x 120 mm (wxhxd) including control unit with standard actuator UP-STOP-DOWN and pulse control incl. self- monitoring safety edge. Counter/error code display and servicing info display in top of control cabinet. Operating speed 0.25 m/s, safety rating IP 55. If there is a power failure, the disengage device enables manual operation at any time.

Options:

Radio remote control

"Open" (if open button is used during closing process - door immediately stops and opens completely)

"Automatic close" (safety photo cell compulsory requirement) Door closes automatically after set period (4-60 sec)

Pull switch for OPEN / CLOSE

External push-button, key switch

"One-button function" - opens or closes door, depending on actual status (e.g. radio, pull

switch)

additional safety (e.g. photo cell, radar) – door immediately opens completely

D-Module (D1-D7)

Photo cell

Reduced opening height

Radar

Magnetic loop

Warning lights

Traffic lights

Interlocking door function

Door/bridge interlock

D-Module (automation module)

D1 functions

red lamps, inclusive, blinking continuously when door is moving

red blinking light before "Automatic close"

constant red light with door closed available

Start time for blinking lights before closure can be set

D7 - function incl.

D2 functions

Magnetic loop, inclusive, with various functions, e.g.

"Safety and checkback signal"

"Open and checkback signal"

"Safety and open"

"Open"

A DIP switch can also be chosen to provide confirmation as additional safety

D7 - function incl.

D3 - functions

Interlocking door function or mutual interlocking between two doors

Door/bridge interlocking

Incl. 24 V AC max. 400 mA for additional units

Relay for "Door open" or "Door closed"

D4 functions

Combination of D1 and D2

red lamps (inclusive) blinking continuously when door is moving

red blinking light (inclusive) before "Automatic close"

constant red light with door closed available

Start time for blinking lights before closure can be set

A DIP switch can also be chosen to provide confirmation as additional safety

D7 - function incl.

magnetic loop (inclusive) with various functions, e.g.

"Safety and checkback signal"

"Open and checkback signal"

"Safety and open"

"Open"

D5 functions

Directional sensor traffic light (including red/green)

Control of oncoming traffic in the doorway

using "Open interior" or "Open exterior" to control oncoming traffic

Oncoming traffic sees alternately red or green light, depending on which "Open command" is given first

D3 - functions

D6 functions

Directional sensor traffic light with magnetic loop activation (inclusive), of "Open exterior"

Control of oncoming traffic in the doorway

using "Open interior" or "Open exterior" to control oncoming traffic

Oncoming traffic sees alternately red or green light, depending on which "Open command" is given first

D3 - functions

D7 functions

Interlocking door function or mutual interlocking between two doors

Door/bridge interlocking

Incl. 24 V AC max. 400 mA for additional units

Relay for "Door open" or "Door closed

Other supplementary equipment

Anti-corrosive hardware

Anti-corrosive package Type "C"

Stainless steel hinges and roller brackets

Stainless steel screws

Stainless steel roller shafts and door cables

Aluminium top and bottom profile

Powder coated corner bracket (RAL 9002)

Anti- corrosive package Type "A"

Stainless steel hinges and roller brackets

Stainless steel screws

Stainless steel roller shaft and door cables

Aluminium top and bottom profile

Powder coated corner bracket (RAL 9002)

Powder coated end caps, trusses, tracks, hangers, connection beams, safety pull bracket (RAL 9002)

Anti- corrosive package Type "S"

Safety pull cables, stainless steel

Anti- corrosive package Type "Z"

Electro-galvanized springs (max. 70.000 cycles)

Cable break device

Increased cycle spring (20.000 – 100.000)

Ventilator "P" (free area approx. 170 cm²)

Special models

Side fixed sections with and without passdoor similar appearance sectional panel door (subject to technical inspection) available on request!!