L20 DOORS/SHUTTERS/HATCHES 
490 AUTOMATIC DOORS:

Company info:

Besam (Manufacturing) Pte Ltd, 33 Ubi Ave 3 #03-52 Vertex Singapore 408868

Tel: +65 6745 6228  Fax: + 65 6745 7322

Email: info@besam.com.sg Web: www.besam.com.sg

Models:
Automatic Sliding Door System (ADS HERMETIC UniSlide-1 Sliding Door Operator), beam mounted with one hermetically sealing sliding door complete with an operator for providing automated operation of the sliding door leaf.

Dimensions:

The Frame Height (FH): XXXXmm

The Frame Width (FW): XXXXmm

The Between Jambs size (COW): to suit FW measurement.

The Clear Opening Height (COH): To suit FH measurement.

The Midrail Height (MH): XXXXmm from FFL

(By others: - Prepared opening).

Lead Lined Door and Frame?   YES     or     NO

Standard equipment:
Operator including normal installation to comply with BS7036. 
Cover type: Cover with PS-5 Key operated 5 position programme selector.

Frame finish: SAA or Besam powdercoat finish RAL ref: To be confirmed

Glass type: Glazed panel with lead lining where applicable

Midrail type: Midrail (150 mm)

Emergency unit: EEU (electrical)

Electric Locking Required:  YES    or   NO

Activation and control system:

Electronic control unit with plug-in connections and power supply.
R1 (directional) entry activator or push pad 
R1 (directional) exit activator or push pad

Safety device(s):

Electronic emergency opening unit.

Automatic reversing.

Two way threshold presence safety system.

Sidelight Safety Devices

Please consult Besam (Manufacturing) Pte Ltd for details and quotation for project specific notes.